Daniela's generic ATAPI Filter - Release 0.3.10
		  -----------------------------------------------


NAME
     DaniATAPI.FLT  -  replacement for IBMIDECD.FLT, IBMATAPI.FLT, DaniADsk.FLT
		       and all other ATAPI related filters.

SYNOPSIS
     This filter driver supports all types of ATAPI devices. It is a superset
     of IBMIDECD.FLT, IBMATAPI.FLT and DaniADsk.FLT, and supports all devices
     that the mentioned drivers do.
     Additionally, all ATAPI devices can be accessed through the OS/2 ASPI
     software interface. Each EIDE channel shows up as a SCSI channel, and
     each ATAPI device as a SCSI device (master = SCSI ID 0, slave = SCSI ID 1).

DESCRIPTION
     This release of my ATAPI filter driver is based on the IBMATAPI.FLT and
     IBMIDECD.FLT sources.

     My enhancements are:

     - can deal with the ATAPI ZIP-250
     - improved ZIP performance (up to factor 4 on ZIP-250)
     - supports arbitrary swapping of 100MB and 250MB media
     - reflects the current media capacity up to FDISK, DISKIO or the like
     - OS/2 boot from ZIP is possible
     - faster 32bit PIO in conjunction with DANIS506.ADD (rel. 1.1.1 or later)
     - Busmaster DMA mode works and is tested with Intel, VIA, AMD, HPT, SiS and
       CMD chipsets until now. Busmaster DMA is available now for ALi as well
       (CD/DVD-ROM is safe, but some chip revisions fail on DMA write
       operations!). Due to hardware limitations there is no 32bit PIO and no
       busmaster DMA possible for ATAPI devices attached to a Promise Ultra
       controller.
     - ATAPI devices appear to the rest of the system as regular SCSI-2 devices
       if used with DANIS506.ADD (rel. 1.1.5 or later). This may be disabled
       globally or individually.
     - advanced "hot-swap" support if used with DANIS506.ADD (rel. 1.1.9 or
       later)
     - support for PCCard (formerly: PCMCIA) ATAPI devices (like the Iomega
       PCMCIA ZIP-250 or the Iomega Click!40)
     - support for PCCard CD writers (CDRecord, RSJ)
     - the translation of old-style 6-byte SCSI commands into their more
       modern 10-byte counterparts is no longer hardcoded. The device is
       sensed now to check if it requires this translation.
     - like DaniS506.ADD, this driver stores boot messages internally for
       later readout. To view them, issue "copy ATAPI$ con:", to dump them
       into a file, issue "copy ATAPI$ anyfile".
     - automatic media unload on shutdown if desired
     - supports up to eight IDE channels
     - supports ATAPI MO drives (tested with Fujitsu 1.3GB drive)
     - supports ATAPI units with more than one logical unit (LUN) built in.
       Examples are the Panasonic/IBM PD drive (tested) or some CD-ROM changers.
     - fix compatibility issues with the increasing number of devices that
       bluntly violate the ATAPI specs.

     This means, all freeware utilites designed to work with SCSI devices
     are supposed to work with ATAPI devices as well:

       CDRecord, CDDA2WAV, TAR, ...

COMMAND LINE OPTIONS
     This driver supports all switches and options that IBMATAPI.FLT supports.

     Syntax Diagram
     --------------
						       +------- /I --------+
			    +------------------+       | +---------------+ |
			    V		       |       | V		 | V
     BASEDEV=DaniATAPI.FLT --+----------------++- /A:n +--+-------------+--+->
			     +--- /!V --------+ 	  +- /EJ -------+
			     +--- /EJ --------+ 	  +- /!SCSI ----+
			     +--- /ZA --------+
			     +--- /!SCSI -----+


       >----------+-------------------------------------+------------------|
		  |	  +----------- /I ----------+	|
		  |	  | +---------------------+ |	|
		  |	  | V			  | V	|
		  +- /U:n +--+-------------------+--+---+
			      +- /EJ ------------+
			      +- /!SCSI ---------+
			      +- /TYPE:x --------+
			      +- /RSJ -----------+


     In most cases, options prefaced with ! can be used with the ! modifier to
     explicitly disable the option.  Options are valid both with and without
     the ! modifer.

     The values in parentheses are the default values if the option is not
     present.

     Options may be prefixed by "-" instead of "/" as well.


     Generic options
     ---------------

     /!V						    (quiet)
	(not) Verbose mode
     /EJ						    (don't eject)
	eject medium at shutdown
     /ZA						    (default mapping)
	map ZIP drive to A:
     /!SCSI						    (export all)
	don't export any ATAPI devices as SCSI devices

     Adapter options
     ---------------

     /A:n						    (n/a)
	Adapter number (0, 1, .. 7)
     /I 						    (off)
	Ignore adapter
     /EJ						    (don't eject)
	eject medium at shutdown
     /!SCSI						    (export all)
	(don't) export ATAPI devices as SCSI devices

     Unit options
     ------------

     /U:n						    (n/a)
	Unit number (0, 1)
     /UNIT:n
	same as /U
     /I 						    (off)
	Ignore unit
     /EJ						    (don't eject)
	eject medium at shutdown
     /!SCSI						    (export)
	(don't) export ATAPI devices as SCSI devices
     /TYPE:x						    (none)
	type definition of swappable units
     /RSJ						    (off)
	RSJ CDROM backdoor


     The export of ATAPI devices as SCSI-2 device can be enabled and/or disabled
     globally, per adapter channel, or per individual unit by adding the options
     /SCSI or /!SCSI. If these options are in front of any /A: option, they
     apply globally. If they come after an /A:x option but before any /U:
     option, they apply to adapter channel x and override the global setting. If
     they come after any /U:y option, then they apply to the single unit y only
     and override both the global and the adapter setting. Default is a global
     visibility of all ATAPI devices as SCSI devices.

     The export is globally disabled also and cannot be overridden if the driver
     is renamed to any name beginning with IBM (case insensitive). This avoids
     confusion of the OS/2 installer if you replace IBMIDECD.FLT on installation
     disk #1 by a renamed version of DaniATAPI.FLT.


     To enable booting OS/2 from an ATAPI ZIP drive, I introduced the new
     /ZA switch ('map ZIP to A:'). It takes effect only if the BIOS has mapped
     the ZIP to drive letter A: in order to boot from it; in all other cases
     the /ZA option is a no-op.

     If there are floppy disk drives in your system, then - as a side effect -
     /ZA remaps floppy drive A: to B:, and floppy drive B: (if present) is
     no longer accessable. Due to limitations in OS2DASD.DMD (?) floppy
     reads and writes are a little 'rocky' in this case.

     A boot from ZIP automatically locks the boot medium in the drive, media
     swapping is no longer possible! This lock is imposed automatically by
     OS2DASD. If you insist to eject the locked medium by the 'eject' command,
     this command obviously is routed into nirvana and causes a kernel trap.


     Some people (like me) don't like media left in removable media devices
     (especially ZIP drives) on system shutdown, but tend to forget to eject
     them before powering down the system. The new /EJ option fills the void. If
     /EJ appears in front of all /A:n options, it acts globally on all devices
     controlled by DANIATAPI.FLT; if /EJ comes after an /A:n but before
     accompanied /U:m options, it acts on all units of that adapter channel; if
     it comes after an /U:m option, /EJ acts only on that particular unit. In
     any case, all units marked by /EJ receive a command to eject inserted media
     on shutdown right after file systems are closed.


     Units marked as "hot-swappable" on DANIS506.ADD's command line (by
     /FORCE /ATAPI) need the new option /TYPE: to advice DaniATAPI.FLT to report
     appropriate device types to the device managers.
     The same applies to PCCard adapter channels (marked as /FORCE /PCMCIA on
     DANIS506.ADD's command line). This is done by additional characters
     designating the supported device types:

       'z' or 'Z': all ZIP drives
       'l' or 'L': the LS-120 drive
       'c' or 'C': all CD-ROM like devices (CD-ROM, CD-R/W, DVD-ROM, DVD-RAM)
       'w' or 'W': all CD writer like devices (CD-R/W, DVD-RAM)

     'W' includes 'C' but additionally enables the features required for proper
     operation of the RSJ CDWriter software even if there is no CD writer unit
     attached at boot time.

     There may be more in the future. Some examples on how to use this option:

     1) You have an IBM ThinkPad 600 and intend to plug a floppy drive, a
	CD-ROM, and a ZIP-100 into its UltraBay. The TPs have got the UltraBay
	connected to the secondary EIDE port. Then you need

	BASEDEV=DaniS506.ADD [other options] /A:1 /U:0 /FORCE /ATAPI
	BASEDEV=IBM1FLPY.ADD /A:0 /FORCE:1 /U:0 /F:1.44MB
	BASEDEV=DaniATAPI.FLT /A:1 /U:0 /TYPE:ZC

	(the adapter numbers above are correct!)

     2) You have notebook which can be equipped with either a LS-120 drive,
	a DVD-ROM, or a CD writer. Then you need

	BASEDEV=DaniATAPI.FLT /A:x /U:y /TYPE:WL

     To pick the correct values for /A and /U have a look at the boot messages.

INSTALLATION
     Just copy DaniATAPI.FLT to bootdrive:\OS2\BOOT and add the line

     BASEDEV=DaniATAPI.FLT

     Make sure that all other ATAPI related drivers are inactive or come
     after DaniATAPI.FLT in your CONFIG.SYS.
     If you prefer chasing icons, you can do the copy using DDINSTAL; you
     still have to tidy up CONFIG.SYS!

     If you intend to run the BootOS utility or to install this filter driver
     on a 8.3-only filesystem, I recommend to rename the driver to DaniATAP.FLT.

INTEROPERABILITY TIPS
     In general, DaniATAPI.FLT is intended to replace all other EIDE ATAPI filter
     drivers. If you need to run another filter driver, there are two choices:

     1) list DaniATAPI.FLT before all other EIDE filter drivers in CONFIG.SYS
	and disable it on a particular adapter by /A:x /I.

     2) list DaniATAPI.FLT after all other EIDE filter drivers in CONFIG.SYS
	and let it control the ATAPI units left over.

***  Unfortunately, many people don't bother to read docs carefully enough or
     at all. So I state it here explicitely once again:

     To make SCSI or ATAPI devices visible to programs, you'll need the
     following two lines to be present in CONFIG.SYS!

     BASEDEV=OS2ASPI.DMD /ALL	    (/ALL makes all devices accessible)
     DEVICE=[path]\ASPIROUT.SYS


     CDRecord:

     There are no further options required if you like to run CDRecord/2, but
     not RSJ with your CD writer. The writer is visible to CDRecord as a
     regular SCSI CD writer by default. Just run "CDRecord -scanbus" to locate
     the CD writer on one of the SCSI buses and memorize its address
     (bus,unit,lun).


     RSJ:

     DaniATAPI.FLT is fully compatible to the RSJ cdwriter filesystem and its
     accompanied utilities. In fact, if you run DaniATAPI.FLT instead of
     RSJIDECD.FLT you can take advantage of the improved data transfer modes
     (32bit PIO and busmaster DMA) on all supported chipsets (RSJIDECD.FLT is
     derived from IBMIDECD.FLT and thus supports busmaster DMA on Intel chipsets
     only). If your CD writer model is listed cddrv.inf you don't even need
     LOCKCDR.FLT; DaniATAPI.FLT reorders its SCSI unit mapping if it finds
     a CD writer unit so that RSJ is happy.

     So there are several choices available (listed in order of preference)

     1) BASEDEV=DaniATAPI.FLT

	This enables full use of the CD writer unit as regular CD ROM device,
	RSJ writer device, and CDRecord writer device. If your particular
	model isn't listed in RSJ's cddrv.inf, then you need to add a line
	reading like this example:

     Plextor "PX-RW8421TS" N/A "PLEXTOR CD-R   PX-W8432" N/A  cdmmc  enabled N/A

	Important is this part ^^^^^^^^^^^^^^^^^^^^^^^, it *must* match the
	SCSI IDENTIFY string of your particular model.

	Caution: some devices return different identification strings for the
	ATAPI IDENTIFY and the SCSI IDENTIFY commands! The former one is shown
	at boot or some ATA/ATAPI tools, the latter one can be seen with some
	SCSI bus interrogators (e.g. "CDRecord -scanbus");

	in case of a pre-3.0 version of RSJ, change the line into

     Plextor "PX-RW8421TS" N/A "PLEXTOR CD-R   PX-W8432" N/A  cdatapi  ATAPI N/A

     2) BASEDEV=DaniATAPI.FLT </!SCSI> or </A:x /!SCSI> or </A:x /U:y /!SCSI>
	BASEDEV=LOCKCDR.FLT

	This disables using the CD writer unit as a regular CD ROM drive. You
	better prevent DaniATAPI.FLT from exporting the CD writer as SCSI device
	by applying one of the /!SCSI options, because it will be exported by
	LOCKCDR.FLT now (too). Both RSJ and CDRecord may use the writer. If your
	CD writer model isn't listed in cddrv.inf, LOCKCDR.FLT from RSJ 3.x will
	autodetect and autoconfigure it.

     3) BASEDEV=DaniATAPI.FLT <other options> /A:x /U:y /RSJ
	BASEDEV=LOCKCDR.FLT

	This is very similar to the section above, but DaniATAPI will install
	an additional backdoor to re-enable regular CD ROM operation via
	OS2CDROM.DMD (or replacements).

***  4) BASEDEV=DaniATAPI.FLT
	BASEDEV=LOCKCDR.FLT
	DEVICE=JJSCDROM.DMD /W

	This is similar to the section above, but DaniATAPI will not install
	the additional backdoor; with the /W option JJSCDROM will grab the
	WORM unit exported by LOCKCDR.FLT.

     5) BASEDEV=RSJIDECD.FLT
	BASEDEV=DaniATAPI.FLT
	BASEDEV=LOCKCDR.FLT

	Now RSJIDECD.FLT will control *all* CD-ROM/R/RW/RAM and DVD-ROM/RAM
	devices, DaniATAPI.FLT all other ATAPI devices. None of the advanced
	data transfer modes are available on non-Intel chipsets which is
	particularly bad on fast CD writers where little impact on CPU load is
	desirable.


     BackAgain/2K:

     DaniATAPI.FLT is supposed to work with ATAPI tape drives. Thus CDSEIDE.FLT/
     BTSEIDE.FLT should no longer be required. Unfortunately BA/2K doesn't
     support the OnStream DI-30 tape drive that I have available so I cannot
     check if DaniATAPI.FLT will work flawlessly with other supported tape
     drives.


     SANE:

     SANE users may find that the SCSI bus number, for their scanner, will
     change when DaniATAPI.FLT is used. You may need to run FIND-SCANNER.EXE,
     and edit the scanner address in the *.CONF file, to correct the address.
     This should be a one time change, unless you switch back to the IBM
     supplied drivers.


     UDF:

     If you see UDF formatting failing like this

       [d:\]format w: /FS:UDF /F
       The type of file system for the disk is CDFS.
       WARNING: Formatting will erase ALL data on this disk.
       Continue (Yes or No)? Y
       Formatting is in progress...Format failed.
       Internal error

     then you probably have to blank the CD-RW before. CDRecord is recommended:

       [d:\]cdrecord blank=fast -eject -speed 10


     FUJITSU MO drivers

     these are obsolete now, everything is handled by DaniATAPI.FLT and the
     DASD manager (both large floppy and partitioned media).

FILES
     DaniATAPI.FLT  The driver itself.
     DaniATAPI.DDP  The device driver profile for DDINSTAL
     DaniATAPI.DOC  The file you are reading right now :-)

     cmprssd\DaniATAPI.FLT
		   The same as above, but LXlite compressed. This one is *not*
		   guaranteed to work on every system.
BUGS
     Hopefully none, but who knows ...

TO DO
     - merge with the base S506 driver

COPYRIGHT
     DaniATAPI - Copyright (c) 2002 Daniela Engert. All rights reserved.

STATUS OF PROGRAM
     DaniAATAPI is freeware.

DISCLAIMER
     YOU ARE USING THIS PROGRAM AT YOUR OWN RISK! I don't take any
     responsibillity for damages, problems, custodies, marital dis-
     putes, etc. resulting from use, inability to use, misuse, pos-
     session or non-possession of this program directly or indirectly.
     I also don't give any warranty for bug-free operation, fitness for
     a particular purpose or the appropriate behaviour of the program
     concerning animals, programers and little children.

     THE SOFTWARE IS PROVIDED ``AS IS'' AND WITHOUT ANY EXPRESS OR
     IMPLIED WARRANTIES, INCLUDING, WITHOUT LIMITATION, THE IMPLIED
     WARRANTIES OF MERCHANTABILITY AND FITNESS FOR A PARTICULAR
     PURPOSE. THE ENTIRE RISK AS TO THE QUALITY AND PERFORMANCE OF THE
     PROGRAM IS WITH YOU.  SHOULD THE PROGRAM PROVE DEFECTIVE, YOU
     ASSUME THE COST OF ALL NECESSARY SERVICING, REPAIR OR CORRECTION.

     Or, in a few words:
     If its good, I am responsible.
     If its bad, its all your fault. ;)

     Permission is granted to redistribute this program free of charge,
     provided it is distributed in the full archive with unmodified
     contents and no profit beyond the price of the media on which it
     is distributed is made. Exception to the last rule: It may be
     included on freeware/shareware collections on CD-ROM, as well as
     on magazine cover CD-ROMs.

     All trademarks mentioned anywhere around here are property of their
     owners and the like ...

AUTHOR
     Daniela Engert

     Internet: "Daniela Engert" <dani@ngrt.de>  (preferred)
     Fidonet: 2:2490/2575  (no support here!)

EPILOGUE
     Suggestions and bug-reports are always welcome. Well ... bug-reports
     are perhaps not *that* welcome ... ;)